## Slide 1: Smart Grid Readiness – Self Assessment Tool (SGR-SAT)
1
1st Meeting of State Level Project Management Units (SLPMU) Representatives of NSGM
SGR-SAT

## Slide 2: Contents
2
This presentation has been prepared under the Technical Assistance titled “Supporting Structural Reforms in the Indian Power Sector (or the Power Sector Reforms Programme)” funded by UK aid from the UK government; however the views expressed do not necessarily reflect the UK government‟s official policies. KPMG is the lead service provider of the Technical Assistance.
Context and Objective
Architecture
Tool Snapshot
Usefulness
1
2
3
4
Applicability & Way Forward
5

## Slide 3: Architecture
Domains are reflective of the key utility functions
(6 functions)
Sub-Domains are processes within each function relevant from the Smart Grid perspective (24 sub-domains)
Tool takes a systems view of the utility from smart grid perspective, and classifies it into three aspects –
domain, sub-domain and maturity level
Maturity level captures the progression across a defined sub-domain
Domain
Sub-Domain 1
Sub-Domain 2
Sub-Domain 3
Sub-Domain 4
Sub-Domain n
Maturity Level
Maturity levels have been classified across 5 levels

## Slide 4: Design Consideration: Six Domains reflect key utility functions
Organization (Utility)
Represented by - (i) vision & strategy; (ii) people/ HR; (iii) Skills and capacities; (iv) mgt. reporting
1
Network
Grid operations
Enabling Grid observability, reliability and quality of power supply
Network & load planning, network (substation & distribution) modernization, communication systems and asset maintenance
Network planning, Asset deployment and Mgmt.
2
3
Customer
Retail
Revenue
Process related to metering, billing, and collection
Customer services and enabling customer engagement & participation
4
5
Regulatory & Policy
This also includes utility‟s external
interaction with policy makers/regulators for enabling investments & ensuring consumer protection
6

## Slide 5: Design Consideration: Capturing the sub-processes within the core functions
Regulatory Interface
Data Privacy and Cyber Security
Consumer Metering & Indexing
DT/Feeder Metering
MDMS and Energy Audit
Billing and Collection
Grid Observability &
Security Mgt.
Power Quality Monitoring
Outage Mgt.
Demand Response
Vision & Strategy
People/ Human
Resources
Training & Capacity Building
Mgt. Reporting & MIS
1. Organization
2.Network Planning, Asset Deployment & Asset Mgt.
3.Grid Operations
6.Regulatory & Policy
Load Growth & Net.
Expansion Planning
Substation Modernization
Distribution System Modernization
Asset Survey and GIS
Communication System Modernization
Asset Maintenance Management
4.Revenue Mgt. & Energy Audit
5.Customer
Consumer Connection Mgt.
Customer Care Infrastructure
Consumer Engagement Program
Net Metering
Domains
Sub-domains

## Slide 6: Design Consideration: Levels within each sub-domain map the journeys as the process matures, hence support defining ‘To-be targets’
3
5
4
1
2
Core business processes and technologies that allow a utility to function are being initiated
Performance measures identified in various domains and technologies are being tested
Successfully implemented best available processes/ technologies at a large scale and further performance improvement being sought
Optimization of processes and technology across the entire network to yield further value
Performance measures show marked improvements from baseline with visibility across the organization

## Slide 7: Tool Snapshot – Domain View (1/2)
L1
L2
L3
L4
L5
Reactive load growth mgt.
No standard process for load forecasting/power flow analysis
Standardized processes and KPIs established for load forecasting/ modelling
Dedicated forecasting software deployed. On-line grid scheduling system implemented
Forecasting S/W integrated with smart metering data
Load flows basis above
Forecasting software integrated with AI/ML and other IT-OT systems to minimize margin of error
No initiation of GIS deployment
Discom using Electromechanical/static relays Load Mgt. System (LMS) under consideration
FPI, Auto Recloser and RMU under consideration. Only manual Load brake switch (LBS) installed
Initial field survey complete and GIS package implemented
At least 10% of numerical relays installed. Investment in LMS initiated
Sectionalizers and RMU installed for at least 5% of total identified population or sites.
GIS database updated with consumer meters and 100% of distribution assets mapped in GIS
LMS integrated with SCADA. 30% of existing relays replaced and integrated with LMS.
Incremental installation (10%) of FPI, AR, Sectionalizer and RMU
GIS integrated with AMS, and MDMS for energy audits
60% of existing relays replaced & integrated with LMS. SAS architecture aligned with IEC standard
Incremental installation (~50%) of FPI, AR, Sectionalizer and RMU
GIS integrated with ERP
90% of existing relays replaced and integrated with LMS. At least 50% of PTs at SS upgraded with OLTC
Incremental installation (~90%) of FPI, AR, Sectionalizer and RMU
Little or no communication with Control Centre and DA components
Incremental addition (5- 10%) in communication link set up at CC and SS level
Incremental addition (10- 20%) in communication link set up at CC and SS level
Incremental addition (~50%) in communication link set up at CC and SS level
Incremental addition (~100%) in communication link set up at CC and SS level
Asset registry exists but not 100% complete. Assets maintained under reactive maintenance
Complete asset register developed. Asset Mgmt. System generates maintenance schedules.
Asset data integrated into GIS as per SOP. AMS integrated with WFMS.
Grid operations factor in Asset Health index
Predictive maintenance based tool introduced to decide on a holistic maintenance strategy
Load Growth & Net. Expansion Planning
Substation Modernization
Distribution System Modernization
Asset Survey and GIS
Communication System Modernization
Asset Maintenance Management
2.Network Planning, Asset Deployment & Asset Mgt.
Maturity levels

## Slide 8: Tool Snapshot – Domain View (2/2)
5.Customer
Maturity levels
Consumer Connection Mgt.
Customer Care Infrastructure
Consumer Engagement Program
Net Metering
L1
L2
L3
L4
L5
o Manual process for new/existing connection mgmt.
o Centralized new connection management activities
KPIs defined and monitored
Online services for new connection.
Improvement in KPIs
Online tracking of new connection application status available
Online monitoring of connection status/maximum demand
Analysis of customer‟s historical data for improving services
Customer help-desk established
Customer care centers IT enabled
KPIs defined and monitored (e.g.: complaint resolution time)
Optimum routing of consumer calls through IVRS, Computer Telephony Integration,
Improvement in KPIs observed
Call center workforce management system implemented
Self-service options such as chat-bots introduced
Customer engagement on reactive basis
Customer segmentation
Trained customer care executives
Engagement activities for pilots
KPIs defined & monitored
Budget allocated
Dynamic website and CRM implemented.
Improvement in KPIs
On-demand information for consumers
Consumer portal available on mobile
Feedback/complaint mgt. system deployed
Social media used for creating awareness
Dedicated staff for handling social media accounts
Development of net metering policy under consideration
Net metering policy developed.
Manual application process
KPIs defined & monitored
Online application & payment services for net metering
Improvement in KPIs
End-to-end online process for net metering application replicated (including agreement signing)
Net-metering application system automatically determines feasibility

## Slide 9: Tool Snapshot – Sub-Domain View (1/2)
Level 3
Level 4
Level 5
Maturity levels (Selection to be made by the utilities)
Level 1 Level 2
Load growth done on reactive basis; and no standard load forecasting/ model established
process
for load
Standard established forecasting
KPIs (like error margin)
defined & are being monitored regularly
Dedicated forecasting
software deployed which
takes into account a
number of factors to
predict load
On-line grid scheduling
system implemented with process in-place to vet
day-ahead schedule exchanges with SLDC
Forecasting integrated with
software
smart
metering data
Sub-transmission and distribution assets
augmentation plans fully aligned with power flow analysis
All zones are covered
Forecasting software's
logic integrated with Artificial
Intelligence/ Machine Learning and
other IT-OT smart grid systems to minimize the margin of error [1-2%]
`
`
Domain:
2.Network Planning, Asset
Deployment & Asset Mgt.
Subdomain:
Load Growth & Net. Expansion Planning
Options to upload existing documents for review

## Slide 10: Tool Snapshot – Sub-Domain View (2/2)
Domain:
5. Customer
Level 3
Level 4
Level 5
Maturity levels (Selection to be made by the utilities)
Level 1 Level 2
Customer customer established
help-desk in Customer care centers care center are IT enabled with
Relationship
Customer Management implemented
KPIs defined (e.g.: Average
resolution monitored
complaint time) & are
on
monthly/quarterly basis
Interactive Response, Telephony automatic
Voice Computer Integration,
call distributor
implemented for optimum routing of consumer calls
Improvement in KPIs due to automation in customer care infrastructure
management
Call center workforce
system
implemented for optimal scheduling of customer care executives
Self-service options such as chat-bots are
introduced
Subdomain:
Customer Care Infrastructure

## Slide 11: Tool Usefulness– Illustrative Example
Creating the As-Is Maturity View (Full-View)
Domain-1: Organization | 
S1-1 | Vision and Strategy
S1-2 | Human Resources
S1-3 | Training and Capacity Building
S1-4 | Management Information System
Domain-2: Network Planning, Asset Deployment & Mgt. | 
S2-1 | Load Growth Study & Network Ext. Planning
S2-2 | Asset Survey and GIS
S2-3 | Substation Modernization
S2-4 | Distribution System Modernization
S2-5 | Communication System Modernization
S2-6 | Asset Maintenance Mgt.
Domain-3: Grid Operations | 
S3-1 | Grid Observability and Security Management
S3-2 | Power Quality Monitoring
S3-3 | Outage Management
S3-4 | Demand Response
Domain-4: Revenue Mgt. & Energy Audit | 
S4-1 | Consumer Metering and Indexing
S4-2 | Distribution Transformer/Feeder Metering
S4-3 | MDMS and Energy Audit
S4-4 | Billing and collection
Domain-5: Customer | 
S5-1 | Consumer Connection Management
S5-2 | Customer Care Infrastructure
S5-3 | Consumer Engagement Program
S5-4 | Net Metering
Domain-6: Regulatory and Policy | 
S6-1 | Regulatory Interface
S6-2 | Data Privacy and Cyber Security
3.00
3.00
3.00
1.00
2.00
3.00
2.00
2.00
2.00
1.00
4.00
1.83
2.00
2.00
2.00
1.00
2.00
2.00
2.25
2.00
2.00
2.00
3.00
2.25
2.00
3.00
2.00
3.00
1.00
2.25
Level 2
Level 3
Level 4
Level 5
Level 1
Peer Average
2
2
2
2
2
2.5
3
2
3
2
2
3
3
2
4
3
3
2.5
3
3
2
2
2
1
3
2
2
2
4
2

## Slide 12: Tool Usefulness– Illustrative Example
Create a To-Be States
Set Targets/Goals
Undertake To-Be Assessment for Each Sub Domain
Analyze
Peer group learnings
Own business objective
Demographic characteristics
Operating Environment, etc.
0
5
1 2
Current Maturity
3 4
Target Maturity
Get Insights on Possible Interventions for Achieving Target
Key Intervention Areas
Implement dedicated forecasting software which takes into account a number of factors to predict load
Implement On-line grid scheduling system and define process to vet day-ahead schedule exchanges with SLDC
Integrate forecasting software with smart metering data
Align the sub-transmission and distribution assets augmentation with power flow analysis
Cover all zones by protection schemes
Load Growth & Net. Exp. Planning
2
Load Growth & Net. Exp. Planning Score
Your Sub-Domain Current Maturity
Overall Domain Targets are Defined
0.0 1.0 2.0 3.0 4.0 5.0
Organization
Network Planning & Asset…
Revenue Mgt. & Energy Audit
Customer
Grid Operations
Regulatory & Policy
Current Maturity
Target Maturity

## Slide 13: Sub-Domain Characteristics and Maturity Implications (Organization
1.1 Vision & Strategy | Definition/ Characteristic | Well-developed utility goals/targets and investment plans incorporating smart grid/IT measures to help guide the management to achieve its business objectives
 | Maturity Implication | The levels track the transition to increased organizational focus on sustainable smart grid/digitization measures and incorporation of new business cases/services
1.2 Human Resources | Definition/ Characteristic | Ensuring right skills and personal are identified and included in the utility for ensuring high productivity in an increasingly ICT driven smart grid operations
 | Maturity Implication | The levels track the transition of workforce to one with increased competencies/skillsets/responsibilities related to overseeing implementation/integration of increased smart grid/IT measures in the organization
1.3 Training & Capacity Building | Definition/ Characteristic | Ensuring that all education and training to develop smart grid competencies across functions and levels are available for its personnel, so that they are ready to address any smart grid challenges
 | Maturity Implication | The levels track the improvement in training practices in the organization to one which actively incorporates current and emerging needs of the sector
1.4 Management Information System (MIS) | Definition/ Characteristic | Enabling monitoring and tracking of key performance metrics and supplying requisite information to the senior management for making informed decisions
Domain)

## Slide 14: Sub-Domain Characteristics and Maturity Implications: (Network Planning, Asset Deployment and Management Domain) - (1/2)
2.1 Load Growth Study & Network Expansion Planning | Definition/ Characteristic | Incorporating techniques of load modelling and forecasting, and power flow analysis for accurate load growth study, basis which network extension planning is carried out. Historical Data from field devices/ metering, weather, usage pattern etc. is used for accurate load modelling and forecasting.
 | Maturity Implication | The levels track increased sophistication, automation and accuracy in load forecasting techniques (including integration with various smart grid data sources)
2.2 Asset Survey and Geographic Information System (GIS) | Definition/ Characteristic | GIS applications allow the user to map, model, run a query and analyze large amount of spatial information within a single database. By enabling increased level of up-to date information mapping with GIS such as customer database and indexing; mapping of electrical distribution network, etc., the utility can provide a number of benefits such as efficiency improvement, loss reduction, improved planning and downtime reduction amongst others
 | Maturity Implication | The levels track an increased adoption/integration of up-to-date GIS application for various utility functions
2.3 Substation Modernization | Definition/ Characteristic | It includes deployment of various components which aids substation automation such as: Numerical relays- Network protection relays protect distribution assets in the event of faults which cause drop in voltage, unbalance and loss of stability of the system. By upgrading to IED based numerical relays, utilities can enable faster disturbance detection, and provide remote supervision & control of asset On-load tap changer– The digital OLTC devices installed at power transformers enable adjusting of the feeder voltage at the substation, depending on the loading condition of the feeders Substation gateway - they provide the communication interface between the electrical substation and the area dispatch centers (SCADA). The main functions of the Substation Gateway is to transmit substation indications and measurements to the dispatch center, and dispatch centers‟ commands to the substation control system. The SAS deployment may be aligned with IEC 61850 architecture, which is an international standard defining communication protocols for intelligent electronic devices at electrical substations.
 | Maturity Implication | The levels track an increased penetration of substation automation devices in the grid and also its integration with SCADA/DMS for effective operations

## Slide 15: Sub-Domain Characteristics and Maturity Implications: (Network Planning, Asset Deployment and Management Domain)- (2/2)
2.4 Distribution Modernization | Definition/ Characteristic | It includes deployment of various components which aids distribution automation such as: Fault Passage Indicator‟s (FPI) are installed across distribution network to identify faults occurring in the downstream section from the point of its installation in the distribution system. With increased coverage of FPI, utility can acquire information regarding the section of the line having fault. This would help it in eliminating the patrolling of entire line for finding the fault, ultimately reducing restoration time and improving the efficiency of outage management system. Recloser are distribution circuit protection devices that provide more accurate and more flexible coordination for faults than can be obtained from traditional fuses. By strategically adding reclosers to the design of distribution circuits, utility can divide the main feeder into a series of load blocks to limit outage effect. Further these devices, by enabling remote control and data acquisition, form a critical part of enabling automatic fault restoration function. Sectionalizers are self-contained and circuit-opening devices used to isolate faulted sections of electrical distribution systems (Sectionalizer cannot interrupt fault current, an upstream breaker or recloser has to operate that). Therefore, by placing Sectionalizers strategically in co-ordination with reclosers, utility can provide the desired protection over a wide range of fault conditions. Ring Main Unit (RMU) enables to protect transformers on the secondary distribution network. The remote terminal units (RTU) installed at RMUs sites allow for control of switching devices such as breaker, isolator switches etc. inside RMU panel from Master station(s). With real time analysis of RMU data through SCADA, it is possible to detect sudden feeder voltages and current changes, any abnormal load variations or physical conditions. This helps utility to reduce installation, maintenance, and operational costs while also reducing the instances of power disruption that result from the sudden malfunctioning of the power grid systems.
 | Maturity Implication | The levels track an increased penetration of distribution automation devices in the grid and also its integration with SCADA/DMS for effective operations
2.5 Communicatio n System Modernization | Definition/ Characteristic | Substation communication systems provide the backbone of the Smart Grid, facilitating real-time monitoring capabilities over feeder heads at substations, feeder distribution automation components and enabling utility to transition to a dual mode (centralized and de-centralized) control over grid operations.
 | Maturity Implication | The levels track an increased penetration of substation fiber-optic communication establishing links with field distribution automation components
2.6 Asset Maintenance Management | Definition/ Characteristic | By evolving asset maintenance strategies to align with smart grid infrastructure, the utility can unlock the capability to link maintenance with asset condition thereby reducing unnecessary maintenance shutdown, track causes of failures, take near-real time corrective actions, more efficiently deploy workforce resources and improve capacity planning performance.
 | Maturity Implication | The levels track a transition from manual, scheduled maintenance practice to one with increased automation and advanced analytics for enabling condition/predictive based maintenance practice

## Slide 16: Sub-Domain Characteristics and Maturity Implications: (Grid Operations Domain)
3.1 Grid Observability & Security Management | Definition/ Characteristic | Observability represents the comprehensive visibility of electrical networks on operator screen though centralized control center Situational awareness relates to the adequate processing and presentation of the huge amount of real-time data from electrical networks so that the insights drawn are helpful to the operator.
 | Maturity Implication | The levels track an increased integration of IT-OT applications for providing increased level of network visibility (real time data) and ability for real time remote control at the centralized main control center
3.2 Power Quality (PQ) Monitoring | Definition/ Characteristic | With traditional infrastructure management of power quality has to rely mostly relied on reactive measures. However, by increasingly adopting advanced communication, data collection, monitoring, and control infrastructure, utility power quality management process should evolve to use analytics based decision making to maintain power quality within the established thresholds. Evolving power quality & reliability management process by adopting advanced monitoring and control infrastructure, and using analytics based decision making to maintain power quality & reliability within thresholds.
 | Maturity Implication | The levels track an increased adoption of field and IT devices for enabling real-time capturing and monitoring of power quality data, including increased adoption of automation for voltage management
3.3 Outage Management | Definition/ Characteristic | A centralized OMS utilizing field level IEDs to enable automatic fault identification, isolation and restoration mechanism with a view to minimizing outage time Although reliability thresholds have been defined, tracking and managing them has been a challenge with traditional infrastructure. As utilities transition to enabling real-time monitoring and control systems, power reliability management should involve into a dedicated function involving analytics based decision making and increased level of automation/ self-healing capability to minimize impact of outages on the grid the established thresholds.
 | Maturity Implication | The levels track an increased adoption of field and IT devices for enabling real-time capturing and monitoring of power outage data, including increased adoption of automation for fault location, isolation and restoration
5.4 Demand Response | Definition/ Characteristic | DR programs can form a major component of utility‟s peak load management strategy. By employing DR programs, utility can benefit through more efficient use of available assets/resources, reducing cost of power purchase and facilitation of higher penetration of renewable energy resources Employing DR as a major component of peak load management strategy with a view to reducing un-scheduled imports, reduced load diversity and facilitating higher penetration of renewable energy resources
 | Maturity Implication | The levels track an increased adoption of demand response program by consumers and also an increased level of automation in DR process

## Slide 17: Sub-Domain Characteristics and Maturity Implications: (Revenue Mgt. & Energy Audit Domain)
4.1 Consumer Metering and Indexing | Definition/ Characteristic | With adoption of Advanced Metering Infrastructure (at consumer level), utility can unlock a range of applications including real-time remote meter reading, & billing etc. Combined with the practice of maintaining up-to date consumer indexing, AMI enables utility to have system wide visibility and enables key smart grid operations like outage management, accurate energy audit, load monitoring etc.
 | Maturity Implication | The levels track an increased penetration of smart meters deployed at consumer level along with the practice of maintain update consumer indexing data
4.2 Distribution Transformer / Feeder Metering | Definition/ Characteristic | With adoption of Advanced Metering Infrastructure (at Distribution Transformer or DT and feeder level), utility can unlock a range of applications including real-time remote meter reading, automatic real time energy audit, power quality monitoring, load monitoring, etc.
 | Maturity Implication | The levels track an increased penetration of smart meters deployed at DTs and Feeders
4.3 Meter Data Management System (MDMS) and Energy Audit | Definition/ Characteristic | A MDMS is a database with analytical tools that enable interaction of smart meter data with other information systems such CIS, billing systems, OMS, GIS, etc. By achieving higher level of software integration and greater penetration of smart meter, utility can enhance the analytics capability of MDMS to provide detailed analysis of losses, load, power quality, etc. at the consumer level. The energy audit tool helps utility in analyzing consumption level data for identifying losses and protecting utility revenues and improving its financial health.
 | Maturity Implication | The levels track an increased integration of smart meter data with other utility systems and an increased level of adoption of smart meter analytics for reducing AT&C losses, improving DT utilization and improving customer satisfaction
4.4 Billing and collection | Definition/ Characteristic | Enabling automation of the entire billing and collection process to reduce errors in billing, collection cycle time and deliver high customer satisfaction/convenience with reduced operational costs
 | Maturity Implication | The levels track an increased adoption of online mode for billing and collection by utility‟s consumers

## Slide 18: Sub-Domain Characteristics and Maturity Implications: (Consumer
Domain)
5.1 Consumer Connection Management | Definition/ Characteristic | Incorporating IT/online based processes in consumer connection management to help the utility in securing higher customer satisfaction levels, saving transaction costs and optimizing use of manpower resources.
 | Maturity Implication | The levels track an increased adoption of online tools for reducing time and cost for managing applications for new/existing customer connections
5.2 Customer Care Infrastructure | Definition/ Characteristic | A centralize, state-of-the art IT-driven customer care platform to provide an efficient and user-friendly customer service. Some of the core applications include: Customer Relationship Management (CRM) systems compile customer data across different channels -- or points of contact between the customer and the utility. CRM concentrates on service-oriented activities such as customer set-up; issue correction; servicing requests for information, etc. CRM systems can also give customer-facing staff detailed information on customers' personal information, bill history and concerns. Interactive Voice Response Service (IVRS) is a telephony menu system that enables identification, segmentation and routing of callers. It is an effective tool to help significantly reduce costs and increase efficiency of customer care center Automated call distributor – this is a an application/device which integrates with IVRS to efficiently distribute/routes inbound calls to most appropriate customer care agents Computer Telephony Integration (CTI) allows interactions on a telephone and a computer to be integrated or coordinated. The most common application of CTI is a “screen-pop” that has the ability to populate the computer screen with caller information and history. Chat-bots - A chat-bot is an artificial intelligence (AI) software that can simulate a conversation (or a chat) with a user in natural language through messaging applications, websites/mobile apps. Chat-bot applications streamline interactions and enhancing customer experience. At the same time, they offer utilities new opportunities to improve the customer engagement process and operational efficiency by reducing the typical cost of customer service.
 | Maturity Implication | The levels track an increased integration of automation/IT tools in customer care operations for increasing customer satisfaction and operational efficiency
5.3 Consumer Engagement Program | Definition/ Characteristic | Incorporating customer engagement as a core part of utility operations for encouraging customers to adopt smart grid technologies actively and thus help unlock full range of smart grid benefits Smart grid requires active consumer participation to unlock full range of benefits. Therefore, as utility transitions to smart grid, incorporating customer engagement as a core part of utility operations becomes important for encouraging customers to leverage and adopt smart grid technologies actively (i.e. enabling them to become more informed, aware of energy usage and participate in utility programs for mutual benefits).
 | Maturity Implication | The levels track an increased level of program focus including increased funding, use of online media, dedicated staff and customer data for delivering a higher level of consumer engagement and participation
5.4 Net Metering | Definition/ Characteristic | Enabling greater choice for customer-owned generation (e.g., solar rooftop) by providing a seamless and consumer-friendly IT based process for implementing net metering policy.
 | Maturity Implication | The levels track an increased adoption of online tools for reducing time and cost of net metering applications and helping increasing consumer adoption

## Slide 19: Sub-Domain Characteristics and Maturity Implications: (Regulatory &
Policy Domain)
6.1 Regulatory Interface | Definition/ Characteristic | Pro-actively seeking regulatory approvals and buy-in required for enabling new services to unlock various smart grid functionalities Departure from traditional business models of smart grid deployment and exploration of new business models which are more efficient as well as financially viable
 | Maturity Implication | The levels track a progress towards pro-active collaboration of utility and regulator to identify, develop and enable operationalization of new business/investment cases based on smart grid technologies
6.2 Data Privacy and Cyber Security | Definition/ Characteristic | Having in place formal guidelines/ processes and structures to promote information security measures and deal with potential vulnerabilities of IT systems, thus enabling confidentiality, integrity and availability of its critical IT infrastructure.
 | Maturity Implication | The levels track an increased adoption of data privacy and cyber security measures by utility in its day-to-day operations

## Slide 20: Utility smart grid maturity assessment survey with criteria – Organization Domain
Maturity Levels
L1
L2
L3
L4
L5
Development of smart grid roadmap/plan under consideration
SG roadmap in-place
SLPMU established.
At least one pilot/POC in- progress
SG training for workforce
Pilot deployed and scale- up plan prepared
ROI of SG business cases measured, documented and shared.
Large scale implementation complete
ROI from SG activities sufficient to sustain future SG opportunities
Organization wide roll-out
New service/ product offerings explored
/integrated
Planned for a team of personnel for SG
SG nodal officer selected
SG cell or core team established.
Roles and responsibilities defined
IT team growth trajectory specified
Ongoing SG projects monitored by core team
Core team engaged in planning and creating larger business cases for SG implementation
SG core team oversees organization wide technology initiatives and takes up new business cases
Sub-Domains
Planning for smart grid training goals under-way
Employees nominated for external training
SG competencies identified
Annual training completed for SG team members/ nodal officers
Defined SG training plan
Training of SG trainers initiated
Initiated strategic tie-ups
Annual SG training program
Review and up gradation of training plans
E-learning programs
Manual processes for data management and reporting
Standalone computer based systems used for data management and reporting
MIS implemented as web-based application
Reporting structures are well-defined
Data collection is automated
MIS is integrated with IT-
OT systems of SG
Generation of reports by
MIS for MoP, CEA etc.
Addition of business intelligence tools
Management dashboards
Vision & Strategy
People/ Human Resources
Training & Capacity Building
Mgt. Reporting & MIS

## Slide 21: Utility smart grid maturity assessment survey with criteria – Grid
Maturity Levels |  |  |  |  |  |  |  | 
L1 |  | L2 |  | L3 |  | L4 |  | L5
Legacy SCADA systems not impactful Manual switching at SS through telephonic commands from CC |  | Implemented modern SCADA and integrated with SAS Disaster Recovery centre Grid status observable at main CC |  | Grid switching operations supported by on-line network security analysis Remote control of SS Operator screens RT data sharing - SLDC Volt-VAR controls |  | Grid switching operations based on smart field sensors/DA Automated Fault Analysis Disaster Recovery centre upgraded to Backup CC |  | Grid Operator screens fortified with Situational Awareness techniques Grid operations based on RT data using WAM Semi-automated dynamic grid operations
Sub-Domains
Operations Domain
Ad-hoc/Manual monitoring of PQ parameters and reliability indicies
5% DTs regularly monitored
KPIs defined and monitored
RT monitoring of PQ parameters at DTs and consumer level
PQ reports for 30% SS, feeders, DTs
Improvement in KPIs
RT monitoring & reporting of PQ at 60%
SS, feeders, DTs
Voltage variations tracked
Marked improvement in KPIs
RT monitoring and reporting of PQ at 90%
SS, feeders, DTs
Automatic tracking of variations
Manual outage monitoring
OMS implemented.
KPIs defined and monitored
OMS integrated with DA
FLISR implemented
Reliability indices
OMS-crew mgmt. app
Improvement in KPIs
OMS is integrated with WFMS.
Marked improvement in grid reliability indices
Automated Crew Tracking system
Predictive intelligence
DR implementation strategy being formulated
Business case developed
Basic DR pilot for 2% of consumers
KPIs defined and monitored
Semi-automated DR for 10% of consumers
Improvement in KPIs
Automated DR for 5% consumers
Semi-automated DR for 20% consumers
Automated DR for 10% consumers
Semi-automated DR for 30% consumers
Grid Observability & Security Mgt.
Power Quality Monitoring
Outage Mgt.
Demand Response

## Slide 22: Utility smart grid maturity assessment survey with criteria – Revenue
Maturity Levels
L1
L2
L3
L4
L5
Sub-Domains
Management and Energy Audit
Static meters installed for consumers
Consumer indexing not yet complete
Consumer indexing complete and formal process defined
Pilot/POC of at least 1000 smart meters
Smart meters installed for 100% consumers under 20% of total DTs
Consumer indexing tool integrated with IT sys.
Smart meters installed for 100% consumers under 60% of total DTs
HAN automation pilot
Smart meters installed for 100% utility consumers
HAN automation rolled out for 15% of consumers
AMR meters installed for at least 50% Feeders and DTs
Smart meters for at least 10% feeders and DTs (or AMR at 100% DTs)
Reports on missing data available
Smart meters for at least 30% feeders and DTs
Smart meters for at least 60% feeders and DTs
Smart meters for 100% feeder and DTs
Legacy MDMS not complying with requirements ((lack of integrated platform/analytics)
Billing system & energy audits are manually managed
MDAS-HES installed and integrated with MDM
Energy audit tool established and integrated with MDM
MDAS-HES/MDM
integrated with billing
system & SCADA
AT&C losses show improvement
Worst performing Circuit technical losses tracked
Tracking by EA tool of DT loading/voltage profile
MDMS integrated with
Consumer Portal
Billing system integrated with customer care sys.
Major improvement in AT&C losses
DT loading well balanced & voltage profiles improve over baseline
Energy Audit tool augmented with consumer loss analytics capability
Manual bill distribution
Development of digital payment options under consideration
Online bills by Email
10% bill collection through digital media
30% bill collection through digital media
Kiosk mode payment collection/ pre-paid metering
50% bill collection through digital media
80% bill collection through digital media
Consumer Metering & Indexing
DT/Feeder Metering
MDMS and Energy Audit
Billing and Collection

## Slide 23: Utility smart grid maturity assessment survey with criteria – Regulatory and Policy Domain
Maturity Levels
L1
L2
L3
L4
L5
State specific SG regulations yet to be notified
Grant based funding of SG projects
SG regulations established
Identified other funding options
Regulatory buy-in for various SG measures
New business cases developed and submitted to regulator for approval
New business case operational leading to increase in revenue
Formulation of initial policy draft in-progress
Customer data privacy policy established
KPIs are defined and monitored
IT policy defined
Cyber threat vulnerability assessment complete
None or minimal instances of security breach
Dedicated team for implementing IT guidelines
Achieved ISO certification
Annual audits for data privacy and cyber security
Reports supporting decision making by senior management
IT/Cyber policy reviewed and updated annually basis risk assessment
Sub-Domains
Regulatory Interface
Data Privacy and Cyber Security

## Slide 24: Smart Grid Maturity Model (Software Engineering Institute at Carnegie Mellon University)
1 2
SGMM is a management tool that provides a common framework for defining key elements of smart grid transformation and helps utilities develop a programmatic approach and track their progress.
o enable
ts,
5 Pioneering | Breaking new ground; industry-leading innovation
4 Optimizing | Optimizing smart grid to benefit entire organization
3 Integrating | Integrating smart grid deployments across the organization
2 Enabling | Investing based on clear strategy, implementing first projects t smart grid
1 Initiating | Taking the first steps, exploring options, conducting experimen developing smart grid vision
0 Default | Default level (status quo)
SGMM Product Suite
SGMM Levels
Global Intelligent Utility Network Coalition (GIUNC) developed SGMM and it is currently under the stewardship of the Software Engineering Institute at Carnegie Mellon University
Source: SEI http://www.sei.cmu.edu/
SGMM would allow utilities to assess their current smart grid position and reach consensus on the direction and pace of their smart grid journey. SGMM provides a guiding framework to utilities in smart grid planning and implementation efforts
3

## Slide 25
SMR
Strategy, Mgmt & Regulatory
Vision, planning, governance,
stakeholder collaboration
OS
Organization and Structure
Culture, structure, training, communications, knowledge mgmt
GO
Grid Operations
Reliability, efficiency, security, safety,
observability, control
WAM
Work & Asset Management
Asset monitoring, tracking &
maintenance, mobile workforce
TECH
Technology
IT architecture, standards, infrastructure,
integration, tools
CUST
Customer
Pricing, customer participation & experience, advanced services
VCI
Value Chain Integration
Demand & supply management,
leveraging market opportunities
SE
Societal & Environmental
Responsibility, sustainability, critical
infrastructure, efficiency
Domains are logical groupings of smart-grid-related capabilities and characteristics for which the SGMM defines a maturity progression. Each level of maturity within a domain is fully described by a set of expected characteristics and a set of informative characteristics.
1 2 3
Smart Grid Maturity Model)

## Slide 26: Smart Grid Maturity Model (Software Engineering Institute at Carnegie Mellon University )
SMR
Strategy, Management & Regulatory
OS
Organization &
Structure
GO
Grid Operations
WAM
Work & Asset Management
TECH
Technology
CUST
Customer
VCI
Value Chain
Integration
SE
Social & Environmental
5
4
3
2
1
0
6 Maturity Levels: Defined sets of characteristics and outcomes
175 Characteristics: Features you would expect to see at each stage
of smart grid journey
8 Domains: Logical groupings of smart grid related capabilities and characteristics
1 2 3

## Slide 27: Smart Grid Definition
An electricity network that uses information and communication technology to gather information and act intelligently in automated fashion to improve the efficiency, reliability, economics, and sustainability of generation, transmission and distribution of electricity*
Smart Grid Definition (As per Proposed Amendment to Electricity Act, 2003)
Advanced Metering Infrastructure
01
Geographic Information System
02
Supervisory Control and Data
Acquisition
03
Distribution Management and
Automation System
04
Smart Grid Enterprise Integration
05
Key Smart Grid Building Blocks